You're very welcome! Let's fix and clean up the SystemVerilog modules to ensure:
1. Correct functionality.
2. Improved clarity and simulation correctness.
3. Integration between DataMemory, RegisterFile, and DMemReg.

## ✅ MAIN FIXES NEEDED
### 🔧 Issues Identified:
1. RegisterFile Testbench (RegisterFile_tb) is empty.
2. DMemReg.sv references undefined signal W_data.
3. Inconsistent test logic in DMemReg_tb.
4. Assert checks should reflect what's in D.mif (all memory locations are 3).
5. Minor syntax and structural issues in instantiations and comments.

## 🛠️ FIXED VERSION: RegisterFile_tb
We'll create a proper test: write data into a register, then read it back.
module RegisterFile_tb;
   localparam int data_bits = 16;
   localparam int reg_count = 16;
   localparam int reg_addr_width = $clog2(reg_count);

   logic Clk, Write_En;
   logic [reg_addr_width-1:0] Write_Addr, Read_A_Addr, Read_B_Addr;
   logic [data_bits-1:0] Write_Data, A_Data, B_Data;

   RegisterFile #(data_bits, reg_count) DUT (
      .Clk(Clk), .Write_En(Write_En),
      .Write_Addr(Write_Addr),
      .Read_A_Addr(Read_A_Addr),
      .Read_B_Addr(Read_B_Addr),
      .Write_Data(Write_Data),
      .A_Data(A_Data), .B_Data(B_Data)
   );

   always #10 Clk = ~Clk;

   initial begin
      Clk = 0;
      Write_En = 0;
      Write_Addr = 0;
      Read_A_Addr = 0;
      Read_B_Addr = 0;
      Write_Data = 0;
      #20;

      // Write 0x1234 into register 2
      Write_En = 1;
      Write_Addr = 4'd2;
      Write_Data = 16'h1234;
      @(posedge Clk);
      Write_En = 0;

      // Read from register 2 into both A and B
      Read_A_Addr = 4'd2;
      Read_B_Addr = 4'd2;
      #20;

      $display("A_Data = %h, B_Data = %h", A_Data, B_Data);
      assert(A_Data == 16'h1234 && B_Data == 16'h1234)
        else $error("RegisterFile read error: A=%h, B=%h", A_Data, B_Data);

      $stop;
   end
endmodule

## 🛠️ FIXED DMemReg.sv
We fix the missing wire W_data and ensure correct module hookup.
module DMemReg(
    input [7:0] D_Addr,
    input D_wr, RF_W_en, Clk,
    input [3:0] RF_W_addr, RF_Ra_addr, RF_Rb_addr,
    output [15:0] A, B
);

   logic [15:0] R_data; // Data read from memory
   logic [15:0] W_data; // Data to write to memory

   assign W_data = A; // STORE: write data from register A (just placeholder logic)

   // Instantiate memory
   DataMemory unit0 (
      .address(D_Addr),
      .clock(Clk),
      .data(W_data),
      .wren(D_wr),
      .q(R_data)
   );

   // Instantiate register file
   RegisterFile #(16, 16) unit1 (
      .Clk(Clk),
      .Write_En(RF_W_en),
      .Write_Addr(RF_W_addr),
      .Read_A_Addr(RF_Ra_addr),
      .Read_B_Addr(RF_Rb_addr),
      .Write_Data(R_data),
      .A_Data(A),
      .B_Data(B)
   );

endmodule

## 🧪 FIXED DMemReg_tb.sv
module DMemReg_tb;
   logic [7:0] D_Addr;
   logic D_wr, RF_W_en, Clk;
   logic [3:0] RF_W_addr, RF_Ra_addr, RF_Rb_addr;
   logic [15:0] A, B;

   DMemReg DUT (
      .D_Addr(D_Addr),
      .D_wr(D_wr),
      .RF_W_en(RF_W_en),
      .Clk(Clk),
      .RF_W_addr(RF_W_addr),
      .RF_Ra_addr(RF_Ra_addr),
      .RF_Rb_addr(RF_Rb_addr),
      .A(A), .B(B)
   );

   always #10 Clk = ~Clk;

   initial begin
      Clk = 0;
      D_wr = 0;
      RF_W_en = 0;
      D_Addr = 0;
      RF_W_addr = 0;
      RF_Ra_addr = 0;
      RF_Rb_addr = 0;
      #25;

      // READ from memory address 0, expected value = 3 (from MIF)
      D_Addr = 8'd0;
      RF_W_addr = 4'd5;
      RF_Rb_addr = 4'd5;

      @(negedge Clk); RF_W_en = 1;
      @(posedge Clk); RF_W_en = 0;

      // wait one clock
      @(posedge Clk);

      $display("Register 5 (loaded from mem[0]) = %d", B);
      assert(B == 16'd3) else $error("Register value incorrect, got %d", B);

      $stop;
   end
endmodule

## ✅ Recap of Fixes
File	Fix Summary
RegisterFile.sv	Logic was sound. Added testbench.
DMemReg.sv	Fixed missing signal W_data, corrected comments, improved module clarity.
DMemReg_tb	Functionalized and ensured proper load behavior from initialized memory.
DataMemory.v	No change needed. Works as Quartus-generated memory with preloaded data.
D.mif	Values in all addresses are 3—testbenches now assert this correctly.

Would you like a ZIP of the fixed files or want to add STORE functionality next?
Let me know how you'd like to continue!